CSC4200/5200 – Computer Networking
Network performance
Instructor: Susmit Shannigrahi
sshannigrahi@tntech.edu

---
Breakout - Questions
Slide 8
Slide 15
Slide 19

---
Recap - Circuit Switching – TDM and FDM
[Speaker Notes: Ndn can help organizing the namespaces Once that’s done, data discovery and provenance is Straight forward Retrieval, transparent failover, and specialized operations In this work, we take a real access log and try to quantify NDN’s improvements to a climate workflow]

---
Circuit vs Packet Switching
Circuit Switching
Dedicated resource divided among participants
Requires setup, guaranteed performance (unless the link breaks)
Packet Switching
Shared resource
Use small chunks of data (packets), send as soon as possible
Store-and-forward packets

---
Frequency Division Multiplexing for Circuit Switching
wikipedia
[Speaker Notes: Ndn can help organizing the namespaces Once that’s done, data discovery and provenance is Straight forward Retrieval, transparent failover, and specialized operations In this work, we take a real access log and try to quantify NDN’s improvements to a climate workflow]

---
Time Division Multiplexing for Circuit Switching
wikipedia
[Speaker Notes: Ndn can help organizing the namespaces Once that’s done, data discovery and provenance is Straight forward Retrieval, transparent failover, and specialized operations In this work, we take a real access log and try to quantify NDN’s improvements to a climate workflow]

---
Packet Switching

---
Statistical Multiplexing for Packet Switching
Ensures that slots will not be wasted
Introduces queuing delay
Breakout:
What actions can you take when queue becomes full? There may be many choices.
Your choice would have profound implications on performance
Drop packets, tell the sender to slow down, direct to another routers

---
How many users can you support?
1Mbps link
Users are active 10% of the time
10 Simultaneous users = full capacity
Circuit switching = 10 users
Packet switching with 35 users < Probability of 10 sim. Users < 0.0004
https://math.stackexchange.com/questions/918861/probability-problem-in-networking

---
Performance - Bandwidth and Latency
Bandwidth = Size of the network pipe
Latency = Delay in sending packets
Throughput = How fast your can send data, function of both bandwidth and latency (and other things)
[Speaker Notes: Ndn can help organizing the namespaces Once that’s done, data discovery and provenance is Straight forward Retrieval, transparent failover, and specialized operations In this work, we take a real access log and try to quantify NDN’s improvements to a climate workflow]

---
Performance - Bandwidth
Bits transmitted at a particular bandwidth can be regarded as having some width:
(a) bits transmitted at 1Mbps (each bit 1 μs wide);
(b) bits transmitted at 2Mbps (each bit 0.5 μs wide).
Packets are made of bits – each bit need some time to be processed at the router. This is transmission delay!
[Speaker Notes: Ndn can help organizing the namespaces Once that’s done, data discovery and provenance is Straight forward Retrieval, transparent failover, and specialized operations In this work, we take a real access log and try to quantify NDN’s improvements to a climate workflow]

---
Performance - Latency
Latency = Propagation Delay + Transmission Delay + Queuing Delay
Propagation = Distance/Speed Of Light (in Copper or Fiber)
Transmit = Size/Bandwidth
How long to “put it on the wire?”
How long to traverse the link?
How long to queue?
[Speaker Notes: Ndn can help organizing the namespaces Once that’s done, data discovery and provenance is Straight forward Retrieval, transparent failover, and specialized operations In this work, we take a real access log and try to quantify NDN’s improvements to a climate workflow]

---
Performance – Queuing Delay
R: link bandwidth (bps)
L: packet length (bits)
A: Average packet arrival rate
Traffic delay = AL/R
AL/R ~ 1
AL/R ~ 0
Everyone in the front has to be serviced first!!!!!
[Speaker Notes: Ndn can help organizing the namespaces Once that’s done, data discovery and provenance is Straight forward Retrieval, transparent failover, and specialized operations In this work, we take a real access log and try to quantify NDN’s improvements to a climate workflow]

---
Performance – Terminology
Bits = b
Bytes = B
Kilobytes = KB (1024 Bytes or 1000Bytes)
Megabytes = MB (1024KB or 1000KB)
Ask ECE folks = 1000, 1Mbps = 1000*1000Bps
Ask CS folks = 1024, 1MB = 1024*1024Bytes
[Speaker Notes: Ndn can help organizing the namespaces Once that’s done, data discovery and provenance is Straight forward Retrieval, transparent failover, and specialized operations In this work, we take a real access log and try to quantify NDN’s improvements to a climate workflow]

---
Performance – Example
Breakout
Calculate the total time required to transfer a 1000-KB file using 1KB packets. Assuming bandwidth is 1.5 Mbps, the RTT of 50 ms, an initial 2 × RTT of “handshaking” before any data is sent.
Delay = Handshake + Transmission + Propagation + Queuing
Delay = 2*50ms + (1000*1024*8)/(1.5*1000*1000) second + 50/2ms + 0 = 5.586seconds
Propagation delay = First bit from sender to receiver
Transmission delay = All bits on the wire
[Speaker Notes: Delay = 2*50ms + (1000*1024*8)/(1.5*1000*1000) second + 50/2ms + 0 = 5.586seconds Propagation delay = First bit from sender to receiver Transmission delay = All bits on the wire]

---
Bandwidth x Delay Product
Capacity of a network pipe = Bandwidth (bits) x Two way Delay (Seconds) (a.k.a RTT or Round Trip Delay)
This is the amount of bits that a pipe can hold!
[Speaker Notes: Ndn can help organizing the namespaces Once that’s done, data discovery and provenance is Straight forward Retrieval, transparent failover, and specialized operations In this work, we take a real access log and try to quantify NDN’s improvements to a climate workflow]

---
Bandwidth x Delay Product - Example
Bandwidth = 50Mbps
Latency = 100ms
Bandwidth x Delay = 50x106x100x10-3 = 5x106 bits = 625 kilobytes
[Speaker Notes: Ndn can help organizing the namespaces Once that’s done, data discovery and provenance is Straight forward Retrieval, transparent failover, and specialized operations In this work, we take a real access log and try to quantify NDN’s improvements to a climate workflow]

---
Bandwidth x Delay - Some more examples
Bandwidth = 54Mbps (Wireless G)
RTT = 1ms
How much data can the pipe hold?
BxD = 54x106x1x10-3
[Speaker Notes: Ndn can help organizing the namespaces Once that’s done, data discovery and provenance is Straight forward Retrieval, transparent failover, and specialized operations In this work, we take a real access log and try to quantify NDN’s improvements to a climate workflow]

---
Bandwidth x Delay – Mars Rover
https://mars.nasa.gov/msl/mission/communications/
https://www.youtube.com/watch?v=NGgzq8eXZOQ
Breakout:
- Bit rate of curiosity: 32000bits/second
- Delay = 14 minutes each way
- BxD = 32000*14*60*2
[Speaker Notes: Ndn can help organizing the namespaces Once that’s done, data discovery and provenance is Straight forward Retrieval, transparent failover, and specialized operations In this work, we take a real access log and try to quantify NDN’s improvements to a climate workflow]

---
And one more thing - Jitter
Also called Interpacket gap
why does it happen (which artifact of packet switching?)
why is it important (think video applications)?
How do you solve this?
[Speaker Notes: Ndn can help organizing the namespaces Once that’s done, data discovery and provenance is Straight forward Retrieval, transparent failover, and specialized operations In this work, we take a real access log and try to quantify NDN’s improvements to a climate workflow]

---
Next Steps
Read Chapter 1
Next lecture – Network performance basics